Position	Length				Meaning					Example
0	11				Frame sync to find the header (all bits are always set)					1111 1111 111
11	2				Audio version ID (see table 3.2 also) / 00 - MPEG Version 2.5 (unofficial extension of MPEG 2) 01 - reserved 10 - MPEG Version 2 (ISO/IEC 13818-3) 11 - MPEG Version 1 (ISO/IEC 11172-3)					11
13	2				Layer index / 00 - reserved 01 - Layer III 10 - Layer II 11 - Layer I					01
15	1				Protection bit / 0 - protected by 16 bit CRC following header 1 - no CRC					1
16	4				Bitrate index (see table 2.1.3)					1001
20	2				Sampling rate index (see table 2.1.2)					11
22	1				Padding bit / If it is set, data is padded with with one slot (important for frame size calculation)					0
23	1				Private bit (only informative)					1
24	2				Channel mode / 00 - Stereo 01 - Joint Stereo (Stereo) 10 - Dual channel (Two mono channels) 11 - Single channel (Mono) / Note: Dual channel files are made of two independent mono channels. Each one uses exactly half the bitrate of the file. Most decoders output them as stereo, but it might not always be the case.					01
26	2				Mode extension (Only used in Joint Stereo) / (see table 2.1.6)					00
28	1				Copyright bit (only informative)					1
29	1				Original bit (only informative)					1
30	2				Emphasis / 00 - none 01 - 50/15 ms 10 - reserved 11 - CCIT J.17 / The emphasis indication is here to tell the decoder that the file must be de-emphasized, that means the decoder must 're-equalize' the sound after a Dolby-like noise suppression. It is rarely used.					00
2.1.1 MPEG Audio Frame Header
The sampling rate specifies how many samples per second are recorded. Each MPEG version can handle different sampling rates.
Sampling Rate Index					MPEG 1				MPEG 2 (LSF)			MPEG 2.5 (LSF)
00					44100 Hz				22050 Hz			11025 Hz
01					48000 Hz				24000 Hz			12000 Hz
10					32000 Hz				16000 Hz			8000 Hz
11					reserved
2.1.2 MPEG Versions and Sampling Rates
The bitrates are always displayed in kilobits per second. Note that the prefix kilo (abbreviated with the small 'k') doesn't mean 1024 but 1000 bits per second! The bitrate index 1111 is reserved and should never be used. In the MPEG audio standard there is a free format described. This free format means that the file is encoded with a constant bitrate, which is not one of the predefined bitrates. Only very few decoders can handle those files.
Bitrate Index			MPEG 1 MPEG 2, 2.5 (LSF) / Layer I Layer II Layer III Layer I Layer II & III
0000			free
0001			32					32		32		32			8
0010			64					48		40		48			16
0011			96					56		48		56			24
0100			128					64		56		64			32
0101			160					80		64		80			40
0110			192					96		80		96			48
0111			224					112		96		112			56
1000			256					128		112		128			64
1001			288					160		128		144			80
1010			320					192		160		160			96
1011			352					224		192		176			112
1100			384					256		224		192			128
1101			416					320		256		224			144
1110			448					384		320		256			160
1111			reserved
2.1.3 Bitrates (in kilobits per second)
In MPEG 1 Layer II, there are only some combinations of bitrates and modes allowed. In MPEG 2/2.5, there is no such restriction.
Bitrate					Allowed modes
free					all
32					single channel
48					single channel
56					single channel
64					all
80					single channel
96					all
112					all
128					all
160					all
192					all
224					stereo, intensity stereo, dual channel
256					stereo, intensity stereo, dual channel
320					stereo, intensity stereo, dual channel
384					stereo, intensity stereo, dual channel
2.1.4 Allowed bitrate and mode combinations
For the calculation of the frame size, you need the number of samples per MPEG audio frame. Therefore, you can use the following table:
				MPEG 1				MPEG 2 (LSF)			MPEG 2.5 (LSF)
Layer I					384				384			384
Layer II					1152				1152			1152
Layer III					1152				576			576
2.1.5 Samples Per Frame
Then you can calculate the frame size like this: / Frame Size = ( (Samples Per Frame / 8 * Bitrate) / Sampling Rate) + Padding Size / Because of rounding errors, the official formula to calculate the frame size is a little bit different. According to the ISO standards, you have to calculate the frame size in slots (see 2. MPEG Audio Format), then truncate this number to an integer, and after that multiply it with the slot size. You can find the correct way of calculating the frame size in the class CMPAHeader in my code. / You get the duration of the file in seconds by applying the following formula: / Duration = File Size / Bitrate * 8 / The method of getting the first frame header in the file and then calculating the duration by the above formula works correctly only for CBR files. / The mode extension is used to join information that is of no use for the stereo effect, thus reducing the needed bits. These bits are dynamically determined by an encoder in the Joint Stereo mode, and Joint Stereo can be changed from one frame to another, or even switched on or off. For all other channel modes, the mode extension field is invalid. / The complete frequency range of MPEG audio files is divided into subbands. There are 32 subbands. For Layers I & II, the two bits in the header determine the frequency range (bands) where the intensity stereo is applied. Within this frequency range, only one channel is stored. All other bands contain information in two separate channels. For Layer III, these two bits determine which type of joint stereo is used (intensity stereo and/or M/S stereo).
Value		Layer I & II					Layer III / M/S stereo Intensity stereo
00		bands 4 to 31					off		off
01		bands 8 to 31					off		on
10		bands 12 to 31					on		off
11		bands 16 to 31					on		on
2.1.6 Mode Extension
2.2. Verifying CRC / If the protection bit in the header is not set, the frame contains a 16 bit CRC (Cyclic Redundancy Checksum). This checksum directly follows the frame header and is a big-endian WORD. To verify this checksum you have to calculate it for the frame and compare the calculated CRC with the stored CRC. If they aren't equal probably a transfer error has appeared. It is also helpful to check the CRC to verify that you really found the beginning of a frame, because the sync bits do in same cases also occur within the data section of a frame. / The CRC is calculated by applying the CRC-16 algorithm (with the generator polynom 0x8005) to a part of the frame. The following data is considered for the CRC: the last two bytes of the header and a number of bits from the audio data which follows the checksum after the header. The checksum itself must be skipped for CRC calculation. Unfortunately there is no easy way to compute the number of frames which are necessary for the checksum calculation in Layer II. Therefore I left it out in the code. You would need other information apart from the header to calculate the necessary bits. However it is possible to compute the number of protected bits in Layer I and Layer III only with the information from the header. / For Layer III, you consider the complete side information for the CRC calculation. The side information follows the header or the CRC in Layer III files. It contains information about the general decoding of the frame, but doesn't contain the actual encoded audio samples. The following table shows the size of the side information for all Layer III files.
				MPEG 1				MPEG 2/2.5 (LSF)
Stereo, Joint Stereo, Dual Channel					32				17
Mono					17				9
2.2.1 Layer III side information size (in bytes)
For Layer I files, you must consider the mode extension (see table 2.1.6) from the header. Then you can calculate the number of bits which are necessary for CRC calculation by applying the following formula: / 4 * (number of channels * bound of intensity stereo + / (32 - bound of intensity stereo)); / This can be read as two times the number of stereo subbands plus the number of mono subbands and the result multiplied with 4. For simple mono frames, this equals 128, because the number of channels is one and the bound of intensity stereo is 32, meaning that there is no intensity stereo. For stereo frames this is 256. For more information have a look at the CRC code in the class CMPAFrame. / 2.3. VBR Headers / Some files are encoded with variable bitrate mode (VBR). To estimate the duration of those files, you have to know the average bitrate of the whole file. It often differs a lot from the bitrate of the first frame, because the lowest bitrate available is used for silence in music titles (especially at the beginning). To get this average bitrate, you must go through all the frames in the file and calculate it, by summarizing the bitrates of each frame and dividing it through the number of frames. Because this isn't a good practice (very slow), there exists additional VBR headers within the data section of the first frame (after the frame header). They contain the total number of frames in the file from which you can calculate the duration in seconds with the following formula: / Duration = Number of Frames * Samples Per Frame / Sampling Rate / Additional to that, the VBR header often contains a table which is necessary to seek positions within the file. / 2.3.1 XING Header / This header is often (but unfortunately not always) added to files which are encoded with variable bitrate mode. This header stands after the first MPEG audio header at a specific position. The whole first frame which contains the XING header is a valid but empty audio frame, so even decoders which don't consider this header can decode the file. The XING header stands after the side information in Layer III files. So you can calculate the beginning of a XING header relative to the beginning of the frame by adding 4 bytes (for the MPEG audio header) to the values from the table 2.2.1. The offset calculation doesn't consider the 16 bit CRC following the header and is equal for all Layers, although only Layer III has a side information. / For reading out this header, you have to find the first MPEG audio header and then go to this specific position within the frame. The XING header itself has the following format. (Note that the position is zero-based; position, length and example are each in byte-format.)
Position				Length				Meaning					Example
0				4				VBR header ID in 4 ASCII chars, either 'Xing' or 'Info', not NULL-terminated					'Xing'
4				4				Flags which indicate what fields are present, flags are combined with a logical OR. Field is mandatory. / 0x0001 - Frames field is present 0x0002 - Bytes field is present 0x0004 - TOC field is present 0x0008 - Quality indicator field is present					0x0007 (means Frames, Bytes & TOC valid)
8				4				Number of Frames as Big-Endian DWORD (optional)					7344
8 or 12				4				Number of Bytes in file as Big-Endian DWORD (optional)					45000
8, 12 or 16				100				100 TOC entries for seeking as integral BYTE (optional)
8, 12, 16, 108, 112 or 116				4				Quality indicator as Big-Endian DWORD from 0 - best quality to 100 - worst quality (optional)					0
2.3.1.1 XING Header
According to this format, a XING header must only contain the ID and the flags. All other fields are optional and depend on the flags which are set. Sometimes this header is also added to CBR files. It then often has the ID 'Info' instead of 'Xing'. / There exists the LAME extension to this header, which is used by the common LAME Encoder, but I didn't take it into account because it isn't necessary for duration estimation. Nonetheless, here is the link for the documentation of the MP3 Info Tag. / 2.3.2 VBRI Header / This header is only used by MPEG audio files encoded with the Fraunhofer Encoder as far as I know. It is different from the XING header. You find it exactly 32 bytes after the end of the first MPEG audio header in the file. (Note that the position is zero-based; position, length and example are each in byte-format.)
Position	Length				Meaning					Example
0	4				VBR header ID in 4 ASCII chars, always 'VBRI', not NULL-terminated					'VBRI'
4	2				Version ID as Big-Endian WORD					1
6	2				Delay as Big-Endian float					7344
8	2				Quality indicator					75
10	4				Number of Bytes as Big-Endian DWORD					45000
14	4				Number of Frames as Big-Endian DWORD					7344
18	2				Number of entries within TOC table as Big-Endian WORD					100
20	2				Scale factor of TOC table entries as Big-Endian DWORD					1
22	2				Size per table entry in bytes (max 4) as Big-Endian WORD					2
24	2				Frames per table entry as Big-Endian WORD					845
26					TOC entries for seeking as Big-Endian integral. From size per table entry and number of entries, you can calculate the length of this field.
2.3.2.1 VBRI Header
3. Additional Tags / Please consider that at the end or at the beginning of the file, there might be additional data which is not part of the MPEG audio frames. This data is called a tag, because it contains metadata about the file, like title, artist, track, years etc. You must consider these tags, because only the MPEG audio data count for the duration estimation.. At the end of a file there might be an ID3V1 tag, a Lyrics3 tag or a Musicmatch tag. At the beginning or at the end of the file there might be an ID3V2 tag and/or an APE tag. You find information about ID3 and Lyrics3 tags at www.id3.org. APE was originally developed for lossless compressed audio files in APE (Monkey's Audio) format. But now this tag is also used for MPEG audio files. The Musicmatch tag was used by older version of the Musicmatch Encoder. Unfortunately there is very little information on the web about this tag, since it is a proprietary format of Musicmatch. / 4. Using The Code / I wrote some C++ classes to handle the MPEG audio frame header and the VBR headers. The class CMPAFile represents the whole file, and provides methods for accessing a specific frame (CMPAFrame class). This class instantiates a CMPAHeader class which represents the MPEG audio frame header of the frame itself. All fields from the header can be accessed via the class variables. Additionally, there is the CVBRHeader class which is the generalization of CXINGHeader and of CVBRIHeader. All tags are derived from the class CTag. These classes are completely independent of any libraries like MFC or ATL. They only use the Win32 API. All classes will throw exceptions in case of errors. All exceptions are of the type CMPAException. You can display information about the exception by using the ShowError() method. All classes use CMPAStream for file-access. This class includes a simple buffer. / Here is a code snippet which demonstrates how you could use these classes. Note that you must at least include the header mpafile.h: / try { / // open file and look for first header / CMPAFile MPAFile(_T("C:\\test.mp3")) ; / cout << MPAFile.GetLengthSec() << _T(" seconds"); / } / catch(CMPAException& Exc) / { / // show error message / Exc.ShowError(); / } / For more information, have a look at the source of the demo project MPEG Audio Info, which is a simple MFC Dialog Application, which uses the class CMPAFile for getting information about a MPEG audio file. It also can perform a check of a whole file for errors within the frame structure.